|  | ......................... pcs. .............................. € .............................. € GEZE overhead door closer TS 5000 L-R 230 V AC, for installation on fire and smoke protection doors, with guide rail BG in 30 mm overall height with electromechanical hold-open device integrated in the guide rail, infinitely and precisely adjustable from 80° in accordance with EN 1155, hold-open position can be overridden, with integrated smoke switch control unit with adaptation of the alarm threshold, soiling indicator and test button, closing force in accordance with EN 1154, closing speed and latching action all adjustable from the front, with adjustable back check, with visual closing force indicator, door leaf installation on opposite hinge side, with mounting plate For lintel height > 1 m, 2 additional ceiling-mounted detectors are required: ( ) GEZE ECwire smoke detector GC 162, 24 V, with 2-wire ECwire technology, complete with base, colour white, tested in accordance with EN 54-7, integrated line monitoring, DIN EN 14637 compliant, can be connected to integrated smoke switch control unit ( ) TS 5000 L closer body size EN 2-6, up to leaf width 1,400 mm, for barrier-free doors according to DIN 18040, up to leaf width 1,100 mm ( ) TS 5000 L ECline closer body size EN 3-5, with very high efficiency > 80 % for barrier-free doors in accordance with DIN 18040, up to leaf width 1,250 mm ( ) TS 5000 SoftClose closer body size EN 2-6, up to leaf width 1,400 mm, for barrier-free doors in accordance with DIN 18040, up to leaf width 1,100 mm, quiet and safe closing even in changing pressure conditions, with one valve integrated in the closer body for the gradual adjustment of the end closing speed for braking or accelerating the door between 15° and 0° Colour: ( ) silver-coloured ( ) dark bronze ( ) white ( ) simulated stainless ( ) RAL … Accessories: ( ) Integrated almost invisible flexible opening restrictor for E/R/ISM guide rails Note: Please note the general building approval from DIBt (German institute for construction technology). |
| --- | --- |
|  | ......................... Pcs. .............................. € .............................. € GEZE FA GC 170 wireless extension for connecting wireless components to GEZE hold-open systems without cables, consisting of: GEZE GC 171 wireless module for connection to GEZE hold-open systems, 24 VDC supply directly via GEZE hold-open system, set up with dip switch without additional programming tools, display of connection quality and status for every device, encrypted wireless connection, wireless integration of up to six devices GC 172 / GC 173 / GC 175 tested in accordance with EN 54-25 and EN 54-18, general type approval for GEZE hold-open systems ( ) GEZE GC 172 wireless ceiling-mounted smoke detector, complete with base, for wireless connection to the GEZE GC171 wireless module, encrypted wireless connection, battery-operated, battery life 8 years, tested in accordance with EN 54-7 and EN 54-25, with adaption of the alarm threshold in accordance with DIN14677, EN 14637 compliant, general type approval for GEZE hold-open systems ( ) GEZE GC 173 wireless ceiling-mounted thermal detector, complete with base, for wireless connection to the GEZE GC171 wireless module, encrypted wireless connection, battery-operated, battery life 8 years, tested in accordance with EN 54-5 and EN 54-25, EN 14637 compliant, general type approval for GEZE hold-open systems ( ) GEZE GC 175 wireless input module for wireless connection to the GEZE GC 171 wireless module, connection to manual trigger switch or potential-free contact of a fire alarm system, encrypted wireless connection, battery operated, battery life 8 years, tested in accordance with EN 54-25 and EN 54-18, installed in flush mounted socket EN 14637 compliant, general type approval for GEZE hold-open systems |
|  | ......................... pcs. .............................. € .............................. € GEZE smoke detector GC 152, 24 V, complete with base, tested in accordance with EN 54-7, integrated line monitoring, conform with DIN EN 14637, can be connected to smoke switch control unit (2 pcs.) Colour: ( ) white ( ) RAL … |
|  | ......................... pcs. .............................. € .............................. € GEZE thermal detector GC 153, 24 V, complete with base, tested in accordance with EN 54-5, integrated line monitoring, conform with DIN EN 14637, can be connected to smoke switch control unit (2 pcs.) Colour: ( ) white ( ) RAL … |
|  | ......................... pcs. .............................. € .............................. € Acceptance test for the hold-open system and permanent attachment of the sign of approval |
|  | ......................... pcs. .............................. € .............................. € Maintenance and testing of hold-open systems (standard) Service package for maintenance and testing according to DIBt approval and according to manufacturer’s specification, with the following features: - One maintenance per contract year - Free provision and updating of the test documents - Attachment of the inspection sticker - Fault diagnosis and repair jobs during the contract period will be carried out at reduced hourly rates - Service technicians will be deployed within 24 hours of the message being received from Monday – Friday between 7 am and 5 pm without surcharges - Personal availability at the help desk 24 hours a day, 365 days a year - Contract run time: 2 years |
|  | ......................... pcs. .............................. € .............................. € Maintenance and testing of hold-open systems (optional position) with warranty extension Service package for maintenance and testing according to DIBt approval and according to manufacturer’s specification, with the following features: - Extension of the warranty to 36 months (condition: the maintenance contract is concluded 3 months at the latest after the commissioning date) - One maintenance per contract year - Free provision and updating of the test documents - Attachment of the inspection sticker - Fault diagnosis and repair jobs during the contract period will be carried out at reduced hourly rates - No separate charging for consumables up to EUR 25 per maintenance service - No separate charging for working hours when spare parts are replaced during the maintenance - Service technicians will be deployed within 24 hours of the message being received from Monday – Friday between 7 am and 5 pm without additional costs (exceptions: Sundays and national holidays) - Personal availability at the help desk 24 hours a day, 365 days a year - Contract run time: 3 years |