|  | ......................... pcs. .............................. € .............................. € GEZE overhead door closer system TS 5000 L-ISM, control in accordance with EN 1158, size 2 – 6, with continuous guide rail BG 30 mm overall height, with integrated mechanical closing sequence control; closing force, closing speed, back check and latching action can be adjusted from the front, with visual closing force display, door leaf installation on opposite hinge side, with mounting plate. ( ) TS 5000 L closer body size EN 2-6, up to leaf width 1400 mm, for barrier-free doors in accordance with DIN 18040, up to leaf width 1100 mm ( ) TS 5000 L ECline closer body size EN 3-5, with very high efficiency > 80% for barrier-free doors in accordance with DIN 18040, up to leaf width 1250 mm ( ) retrofit kit ECline ISM/ISM BG, opening assistance for use on the active leaf, considerable drop in opening torque Colour: ( ) silver-coloured ( ) white ( ) stainless steel optic ( ) acc. to RAL Accessories: ( ) Integrated almost invisible flexible opening restrictor for E/R/ISM guide rails |
| --- | --- |
|  | ......................... pcs. .............................. € .............................. € GEZE carry bar CB flex with GEZE door closer design, for guaranteeing the correct closing sequence for all 2-leaf GEZE door closer systems with door closing sequence control, length in installed state is infinitely variable adjustable (70 - 210 mm overhang), non-visible hinge and length adjustment mechanisms, with cover cap at the side, can be cut to size on site, painted surface as standard. Colour: ( ) silver-coloured ( ) acc. to RAL |